Cherokee Springs Central Control Upgrade

Scope of Work

Central Control Upgrade:

A. TORO Lynx TouchNet Upgrade #LX-00-1-11 N.B. tuned to proper

Frequency with mapping software for OSMAC Basic complete with

specified premium computer, 1 year technical support, and (2) HT-1250

radios with DTMF and tuned to proper frequency.

B All central equipment shall be surge protected with the following

D & B Power Assoc. (Batavia, IL) equipment:

Central Station Protection:

DB42003 – Receptacle protector

DB24001 – RJ II jack protector 200V

DB90607 – RF BNC cable protector

DB90606 – RJ II jack protector 10V

Base antenna, antenna structure coaxial cable, lightning protection,

ground rods, central UPS, and other items shall all be supplied and

installed as per manufacturers recommendations: as per survey for

proper operation of said systems. Contractor shall be responsible for

any items, mentioned or not, for the operation of either specified

radio system.

d. FCC licensing and frequency shall be supplied by Contractor and

performed by qualified agent, at no additional cost to the Owner.

Some troubleshooting of existing satellite controllers on back nine. Controllers will be shown at pre-bid meeting.