NanoLumens LED Ticker

Introduction:

Cherokee Nations Hard Rock Hotel and Casino in Tulsa is accepting bids for an LED ticker.  The ticker will be installed around a square, sheet rocked column.  Each side of the column is 46.5” in width.  Ticker will be installed approximately 10’ above floor.  Viewable surface will meet up at the corners making a tight 90 degree angle with minimal spacing, approximately 1/8”.  The ticker will have built in processing and software for creating content.  Power and network will be provided by customer.  This bid will be for equipment and complete turnkey installation.  Equipment must match specifications below:

Specifications:

| Manufacturer- | NanoLumens |
| --- | --- |
| Product- | NanoSlim |
| Viewable Height in Inches- | 6.24 |
| Viewable Width in Inches- | 199.56 |
| Diagonal inches- | 199.66 |
| Pixel Pitch- | 6.6 Thin |
| Total Pixel Count- | 18,432 |
| Est. Weight lbs.- | 48 |

Est. Frame Thickness in Inches-						4.00

Color Temp-								6500K