Executive Conference Room AV Upgrade

Overview

Accepting bids to procure and install an AV system in the executive conference room. This work includes procurement, installation and programming of the below listed equipment.  Equipment cannot be substituted.

| Quantity | Description |
| --- | --- |
| 1 | Sharp LC90LE657U 90” LED HDTV |
| 1 | Chief XSMU X-Large Fusion Wall Mount |
| 1 | AMX DVX-2155HD-T All in one Switcher |
| 1 | AMX MST-701 Desktop Touch Panel |
| 2 | AMX HPX-900SL Tabletop Pockets (Custom details below) |
| 2 | AMX pocket module- Retractable HDMI |
| 2 | AMX pocket module- Retractable VGA with 3.5mm audio |
| 4 | AMX pocket module- Retractable Ethernet |
| 2 | AMX pocket module- Power outlet |
| 2 | AVB-TX-Multi-DXLINK Transmitter |
| 1 | Sharp BD-HP75U Blu-Ray Player (“Or equivalent”). |
| 4 | JBL Control 16 c/t speaker (white) |
| 1 | Vaddio 999-8800-000 Ceiling mic array (white) |
| 1 | BSS Audio BLU-102 Signal Processor (telephone hybrid and BLU link) |

Installation Details:

Existing AV equipment and cabling will be removed by CNE. Contractor will be required to install new cabling; shielded CAT6 cabling and a minimum size of 14 gauge speaker cable is required.  All high voltage power is in place.  CNE will provide cabling paths from the conference table to existing equipment rack via conduit.  Cabling from rack to 90” display will be routed above drop ceiling.  JBL speakers will be installed in drop ceiling tiles.  AMX pockets will be fitted into table top. Touch panel design must stay consistent to existing properties panel design.  Programming of the BSS audio processor will include ceiling mic array for telephone conferencing along with all other conference room audio sources.  Installation and programming will need to be completed in a 12hr period and be performed during overnight hours. This is a complete turnkey installation.  Contractor will be required to provide system operation training upon completion of installation.  Contractor must provide a minimum one year parts and labor warranty on the installation.