Hard Rock Center Bar Video Wall

# Introduction

Currently at the Hard Rock Center Bar we have a video wall. The video wall will be replaced with a Planar system using all associated material/equipment needed to accomplish the install.  The video walls will be controlled by the existing AMX control system. This bid can be submitted as Installation Only or Parts Only or Installation and Parts.

# Parts

QTY	Manufacturer	Part #		Description

9 	Planar			 LX46HDL 	Clarity Matrix 46" 1920x1080,

LCD video wall system. Includes 1 LCD

module, required power supply, quad

controller electronics and mount.

Landscape Only

1	 Planar 		Cable Set 	Cable Sets for Matrix LX46HDL

1 	Planar 			Trim Kit 3x3	Cosmetic Trim for Matrix LX46HDL

LX46HDL	Landscape Only.

1 	Vaddio 		999-5643-000 YPbPr to DVI/HDMI Format Converter

# Installation Approach and Conditions

The approach to this project must be one that is suitable for a retrofit 24/7 operation.  This Bar will not shut down for this installation and it is imperative that the installation is completed in a neat and clean, dust free manner.  The current ceiling height in the area is approximately twenty-five feet high.

It is the responsibility of the contractor to complete a site survey to evaluate current site conditions.  This installation is required to be a turnkey demolition and installation of the required video wall.

# Roles and Responsibilities

It is the responsibility of the contractor to provide a turnkey installation of the required video wall to include but not limited to the following:

- Demolition of existing equipment

- Installation and purchase of required cabling

- Coordination of all required high voltage power for video wall

- Procurement and Installation of Displays

- Procurement and Installation of Display Mounts

- Procurement and Installation of any and all miscellaneous equipment and materials to provide complete turnkey video wall as described.

Remove the existing video wall and prepare for storage (boxing, wrapping, etc.). Install video wall using Planar equipment and any associated material/equipment needed for the install. This wall will be a 3x3 using Planar Clarity Matrix LX46HDL.

# Testing and Training

This project requires the contractor to provide owner verified proof of performance and training of the complete installation.

# Documentation & Warranty

Please provide the following:

- Video Wall Layout Elevation

- Single Line Schematic of all connections, video and control

- As-built drawings of cable routing and installation details

- Warranty Letter to include equipment warranty dates and installation warranty dates