Scope of Work.

Cherokee Nation Property Management is seeking qualified Structural Engineering/Design firms for 3rd party inspections for the new W. W. Hastings East Hospital in Tahlequah, Oklahoma.

The new hospital will be a 156,486 square foot, three story facility located east of the current W. W. Hastings Hospital.

- The first floor is 85, 478 square feet and will house the lobby, dining, outpatient waiting areas and central plant as well as the imaging, ED, Endoscopy, Surgery and Surgery Clinic Departments.

- The second floor is 35, 504 square feet and will house the Med Surge and ICU Departments.

- The third floor is 35,504 square feet and will house the Women’s/OB Departments.

The structure system will consist of a steel frame with a slab on grade on the first floor and a composite floor system on the second and third floor.  A mechanical penthouse will reside above the third floor hardened roof assembly and the roof assembly will be 1 ½” steel deck supported by steel beams is defined in the Schematic Design Quality Profile.

Initial plans to harden the hospital consist of utilizing 8” thick solid precast concrete wall panels supported from the steel structure and a composite steel and concrete roof structure.  All exterior windows will be laminated glass and will be designed to meet increased wind speed ratings.  Some interior walls will be hardened and are anticipated to be constructed with 8” to 10” thick site-cast concrete.  The generator that serves the hospital will be enclosed in a hardened structure.

Refer to Schematic Design Drawings and Narrative for further detail.

The work will consist of:

- Review approved design plans and specifications to determine all field quality control items that need to be included in the scope of work.

- Observe reinforced steel placement.

- Observe field welding and bolted structural steel connections.

- Provide all reports of testing and note deficiencies of tests.

- Structural 3rd party inspector will conduct peer review of the current set of structural construction documents (plans and specifications). Review to consist of general structural compliance with IBC 2009, the geotechnical report and constructability standards.

- Review of shop drawings, including structural steel, foundations, rebar, exterior LT Gauge framing.

- Generate review comments for owner, construction and design team.

- Provide one (1) subsequent review of the 100% construction documents to ensure incorporation of previous review comments.

- Participate in construction team progress meeting in person or via conference call as needed.

- Provide site inspections during foundation pours, structural steel erection and exterior wall construction and ass needed

- Selected firm will work with Project Architect, Construction Manager, and Cherokee Nation Property Management on issues or concerns as necessary.

Proposal should be based on 20 site visits and 2 drawing plan review.  Bids will be evaluated as base fee for the first 20 visits.  A cost per trip fee will also need to be submitted for any additional above the required 20 site visits.   The price /trip are to include:  trip cost, meals, hotel, site inspection and report, overhead/profit, (i.e.,” value is all inclusive”).

Firms are to submit their hourly rate sheets for key personnel.