Work is to be done in accordance with drawings and specifications as provided by 1Architecture, LLC.

Unless specifically excluded below, the scope of the project shall consist of:

- All work, supervision, labor, supplies, tools equipment, light, water, fuel, power, heat, transportation or other facilities necessary for the construction of the trail alignments as defined in the attached Contract Documents, dated January 3, 2017.

- Staking, clearing and grubbing of the revised portions only of the Primary and Secondary trail layout per Addendum 01 dated 2.17.17. Staking of the revised layout to be done using a GPS locating device with an Autocad Trail Layout File.

- Staking and clearing of the entirety of the primitive trail layout is included in this scope of work. Staking of the primitive trails to be done using a GPS locating device with an Autocad Trail Layout File.

- Removal of all downed trees and brush debris resulting from the previous clearing and grubbing of the Primary and Secondary Trails.

- Removal of all downed trees and brush debris within 10 feet of each side of the Primary, Secondary and Primitive trails measured from the centerline of the trails (20 feet total).

- All downed trees and brush debris listed to be removed in this scope shall be used by the contractor for mulch in the Secondary Trail construction.

- All other work associated with the drawing and specifications.

Exclusions from the scope of the project:

- Trail markers are not included in the scope of the project.

- Staking, clearing and grubbing of the remaining portions of the Primary and Secondary Trails not specifically revised and clouded per Addendum 01. This work has already been performed.

- Trail Parking is not included in the scope of the project.

This is a lump sum bid for all work. The General Contractor will have to adhere to the Code of Conduct established by Cherokee Nation Entertainment along with all insurance and bonding requirements as set forth in the bidding documents.