Statement of Work

| Date | 2/5/18 |
| --- | --- |
| Contact | Stephanie Shults 918 384 7455/stephanie.shutls@cnent.com |
| Job Name | CAT – Guitar Pylon Brand Standard Updates |

Summary

The winning bidder will supply parts, installation and labor to update the red painted ring and neon on the Hard Rock logo badge located on the guitar pylon sign.

This includes, but is not limited to, re-painting the red ring and purple circle to HRI specified gold and purple as well as replacing the red neon with gold LED lighting product.

Project Scope

This SOW covers the following components, activities, deliverables and assumptions.  Included in this will be hardware procurement as well as labor to retrofit the sign with an LED lighting product and repaint red ring and purple circle within the Hard Rock logo badge.

Components:

- Contractor Provided:

| Description | MFR | MFR P/N | QTY |
| --- | --- | --- | --- |
| Sloan Flexibrite LED - Noviol Gold | Sloan LED | 701499C-Y | N/A |

- Miscellaneous – Contractor will provide all miscellaneous components to complete the install.

Tasks:

- Removal – Contractor is responsible for removal of existing red border neon lighting that currently outlines the Hard Rock logo badge.

- Installation – Contractor will retrofit existing red border neon on logo circle and letters with Sloan Flexibrite LED (Noviol Gold).

- Repainting – Contractor will repaint Red ring and purple portion of circle in the logo with brand standard Gold and Purple using PMS 668C Purple and PMS 117C Gold.

Deliverables

- Updated sign elements per the SOW.

- Warranty letter to include equipment and installation warranty dates.

Key Requirements

- Contractor has all necessary tools to accomplish tasks associated with the project.

- Contractor understands and agrees to late night and/or overnight working hours.

- Specified Parts:

  - No substitutions allowed unless owner permission is provided in writing.