Statement of Work

| Date | 10/9/19 |
| --- | --- |
| Client | Cherokee Nation Entertainment (CNE) |
| Job Name Location | Hard Rock Live Entry Sign TVs Catoosa, OK |

Summary

Vendor will provide parts and labor for furnishing the new Hard Rock Live entry sign with 65” displays.

Project Scope

This SOW covers the following components, activities, deliverables and assumptions.  Included in this will be hardware procurement and installation of new equipment.

Components:

- Contractor Provided

| Description | MFR | MFR P/N | QTY |
| --- | --- | --- | --- |
| LG 65” TV | LG | 65UT640S | 4 |
| TV Mount | Chief | MTM1U | 4 |

- CNE Provided

| Description | MFR | MFR P/N | QTY |
| --- | --- | --- | --- |
| Content Player and video cabling. |  |  | 2 |

- Miscellaneous – Contractor will provide all miscellaneous components to complete the install.  This includes, but not limited to j-hooks, brackets, custom panels, labels, hardware, tie wraps, etc.

Tasks:

- Installation – Contractor will install all necessary components to complete the project.

  - Conditions

    - Contractor is responsible for keeping all work areas clean.

  - Equipment

    - Install (4) TVs into sign (photos and design drawing of sign below, backing brackets were designed to fit with specified mount.)

    - Velcro content players to back of displays and dress cabling

- Testing – Contractor will perform complete system test to provide CNE verified proof of performance.

- Training – Contractor will train CNE personnel on all system functions.

Deliverables

- Provide a Warranty Letter to include equipment and installation warranty dates.

- Provide all equipment manuals, any associated software discs, and any unused components.

Key Requirements

- Contract personnel doing work on site and/or remotely must have a current CNGC gaming license.

- Contractor must have taken the CNE lift safety class to use a CNE lift.