ADDENDUM #01

RFB – ROOF PROJECTS HUMAN RESOURCES/OSIYO TRAINING ROOM

12/06/19

QUESTIONS SUBMITTED BY DEADLINE

Question: Who is responsible for disconnection and reconnect on side discharge AC units on human resource roof? The training room roof is flat but can accommodate a 1/8" taper system to promote positive drainage.

Answer: Cherokee Nation electrician will handle this, the contractor will work closely with our electrician to schedule this.

Question:  HR Building:  Specs state replace all cap metal. (Not going to be able to match existing metal because of sun fading). Building has 1/4" taper system existing over entire roof. Need to clarify that this roof gets removed completely down to deck and is to be reinstalled per specifications. 1/4" tapered system with crickets between drains. Base ISO over entire deck is 1.5". Mechanically fasten ISO and fully adhere TPO system. CN is wanting a 20 year Manufacture Weathertight Warranty. As the specs read you are going to get a material 20year standard warranty.

Answer: Color samples to Cherokee Nation as stated in spec, roof is to be removed down to deck.

Question:  Also the A/C units will have to be removed to tear off under them. They need to be disconnected by CN Personnel and lifted by contractor. The only reason I am saying this is because of the conversations on the roof between roofers.

Answer: Cherokee Nation electrician will coordinate this work with the contractor.

Question: Osiyo Roof: Specs state replace all cap metal. (Not going to be able to match existing metal because of sun fading). The existing roof cored out to be 1/2" Perlite. Highly recommend a minimum 1" with a 1/8" taper system sloping to the drains. CN is wanting a 20 year Manufacture Weathertight Warranty. As the specs read you are going to get a material 20year standard warranty. Mechanically fasten ISO and fully adhere TPO system.  A/C units are high enough on this roof that they do not need to be lifted.

Answer: Color samples to Cherokee Nation as stated in spec and 60mm in thickness as stated.