Statement of Work

| Date | 12/2/2019 |
| --- | --- |
| Client | Cherokee Nation Entertainment (CNE) |
| Job Name | Hard Rock Hotel & Casino Tulsa – Add Lights to Amp Bar |

Summary

The winning bidder will supply all parts and install of AV systems for adding four moving lights in Amp Bar at Hard Rock Hotel and Casino, Tulsa.

This includes, but is not limited to, installing all AV equipment and testing all systems for proper functionality.

Project Scope

This SOW covers the following components, activities, deliverables and assumptions.  Included in this will be hardware procurement, labor to install new equipment, programming, implementation, and testing.

Components:

- Contractor Provided: With the exception of “CNE Provided” items in section two below, the procurement of all other parts is the responsibility of the contractor.

| Description | MFR | MFR P/N | QTY |
| --- | --- | --- | --- |
| Chauvet Rogue R2X Spot | Chauvet | ROGUER2XSPOT | 4 |
| Custom Amp Bar Gobo for Chauvet Rogue R2X Spot | N/A | N/A | 4 |
| Custom Amp Bar Gobo for Martin Rush MH1 Profile Plus | N/A | N/A | 2 |
| Mounting Hardware, Cables, Connectors, etc. | N/A | N/A | 1 |

- Miscellaneous – Contractor will provide all miscellaneous components to complete the install except the specific items listed in “CNE Provided” section above.  This includes, but not limited to, cables, connectors, j-hooks, brackets, custom panels, labels, hardware, tie wraps, etc.

Tasks:

- Installation – Contractor will install all necessary components to complete the project.

  - Conditions

    - Work schedule will be coordinated with CNE

    - Contractor is responsible for keeping all work areas clean.

  - Equipment – Contractor is responsible for installing all components needed to complete the project.  Label all equipment with appropriate names and network information as applicable.

    - Install (4) moving lights to various locations at Amp Bar.

    - Install (1) custom gobo in each light, as well as, replace the Center Bar gobos in the (2) existing Martin Rush MH1 lights.

- Programming – Program the DMX address of each light upon installation.

  - DMX addresses will be provided by CNE.

- Testing – Contractor will perform a complete system test to provide CNE verified certificate of compliance.

- Training – Contractor will train CNE personnel on all system functions.

Deliverables

- Provide a Warranty Letter to include equipment and installation warranty dates.

- Provide all equipment manuals, any associated software discs, and any unused components.

- Source code - CNE will take ownership of all environment workspace, library, include, IR, module, and source code files.  At time of final implementation and testing, all code will be loaded to CNE jump server, compiled and loaded to all devices from jump server.

- As built documentation – CAD files to be in AutoCAD DWG format, text files to be in MS Word or MS Excel format, graphic files to be in PNG format.  PDF prints of all documentation should be included with for distribution as needed.

Key Requirements

- Contract personnel doing work on site and/or remotely must have a current CNGC gaming license.

- Contractor has all necessary software tools to accomplish tasks associated with the project.

- Contractor understands and agrees to late night and/or overnight working hours.

- Specified Parts:

  - No substitutions allowed unless owner permission is provided in writing.