Cherokee Nation Businesses is requesting bids for three tornado shelters:

- 2- Above ground shelters for 200 person occupancy to be located at Will Rogers Downs,

20900 S. 4200 Rd, Claremore, OK.

- 1-Above ground shelter for 160 person occupancy to be located at Cherokee Casino,

1621 W Ruth Ave, Sallisaw, OK.

Shelters will be located outdoors.

Concrete pad and foundation by Owner. Bidding firm to supply foundation and pad requirements with proposal.

Shelters must be FEMA, ICC-500, NSSA, compliant.

Shelter design must have current F-5 impact verification from the Texas Tech University National Wind Institute, for the model provided for installation (documentation required).

Shelters must be ADA accessible.

Doors must have the ability to disengage the outer door handle from inside of the shelter.

Pre-finished coat on shelter that is rust and corrosion resistant.

Shelters must be 6’8” or taller interior.

Fold-up bench seating provided

Owner will provide exact location on property.

Installation must be completed by March 22, 2019.

Special Instructions for Will Rogers Downs:

Shelter plans will need to be submitted to Oklahoma State Fire Marshal’s Office for approval.

In addition, there may be certain restricted work times prior to 11am.

Workers will be required to obtain an Oklahoma Horse Race Commission license prior to starting work. There is an OHRC licensing office on-site behind the Casino.