SCOPE OF WORK

Cherokee Nation Property Management is seeking proposals from qualified grading and paving contractors for the patching and resurfacing for the parking lot at the Restaurant of the Cherokees in Tahlequah Oklahoma.

The work will consist of:

- Milling the failed Asphalt paving areas at an approximate depth of two inches (2”), compact soils and patch with asphalt.  Areas to be walked with CNB Project Manager to determine areas to be patched.

- Cleaning the lot of dirt, vegetation and loose debris.

- Apply tack coat using SS-1 emulsion.

- Install two inches (2”) of Type ‘C’ Hot Mix Asphalt, rolled and compacted.

- Restripe parking area using traffic paint per existing layout to include approx. 1,000 LF of 4” line and 6 handicap block, border and symbol, and 19 existing wheel stops.

- Furnish and install 18 wheel stops (6” length) and paint yellow.

- The size of the work area is approximately 24,700 SF.  This is an estimate and contractor is responsible for verifying actual square footages.

- Pick up and cleanup work area at the end of each work day and store material in a manner that is safe for all pedestrians.

- Contractor is responsible for hiring a testing firm to conduct material and density testing requirements as part of their bid proposal.

- Contractor is to provide a proposed work schedule.  This project will have liquidated damages applied to the contract.

This is an occupied building, where patron and guests will be in and out daily.  Contractor is to follow all state and federal laws and laws related to a safe working environment.

Selected firm will work with CNB corporate Construction, Building occupants and Cherokee Nation Property Management Facilities to coordinate schedules and work areas, issues or concerns as necessary.

Fees

Lump sum fee for the above scope and is to include all labor and material necessary to complete the job.  Contractor is to provide warranty for work and materials.

Changes or additional work is not to commence without prior approval.