Statement of Work

| Date | 3/29/2019 |
| --- | --- |
| Client | Cherokee Nation Businesses (CNB) |
| Job Name | Brookhaven GA – Office Network Infrastructure |

Summary

Cherokee Nation Businesses, LLC a wholly owned tribal company of the Cherokee Nation, is seeking qualified bid responses for a turnkey process to pull, install and test/certify data and fiber drops. Install 1 comm rack, ladder if needed, wire management, and patch panels in IDF. The location of the office is 2970 Clairmont Rd, Suite 530, Brookhaven, GA 30329. Start date approx. May 2019

Standards

In general, the following standards at a minimum shall be observed for telecommunications infrastructure and are incorporated herein by reference:

ANSI/TIA/EIA - 568-B.1, Commercial Building Telecommunications Cabling Standard Part 1: General

Requirements, April, 2001

ANSI/TIA/EIA - 568-B.2, Commercial Building Telecommunications Cabling Standard Part 2: Balanced

Twisted-Pair Cabling Components, April, 2001

ANSI/TIA/EIA - 568-B.2-1, Commercial Building Telecommunications Cabling Standard Part 2: Balanced

Twisted Pair Cabling Components, Addendum 1 – Transmission Performance Specifications for 4-pair

100 Category 6 Cabling

ANSI/TIA/EIA - 568-B.3, Commercial Building Telecommunications Cabling Standard Part 3: Optical

Fiber Cabling Components, March, 2000

ANSI/TIA/EIA – 569-A, Commercial Building Standard for Telecommunications Pathways and Spaces,

February, 1998

ANSI/TIA/EIA – 570-A, Residential Telecommunications Cabling Standard, October, 1999

ANSI/TIA/EIA – 606-A, Administration Standard for Telecommunications Infrastructure of Commercial

Buildings, February, 2002

ANSI/TIA/EIA – 607, Commercial Building Grounding and Bonding Requirements for

Telecommunications, August 1994

ANSI/ TIA/EIA – 758, Customer-Owned Outside Plant Telecommunications Cabling Standard, April 1999

BICSI - TDMM, Building Industries Consulting Services International, Telecommunications Distribution

Methods Manual (TDMM)

National Fire Protection Agency (NFPA – 70), National Electrical Code (NEC) –2002

Project Scope

This SOW covers the following components, tasks, deliverables and assumptions.  Included in this will be procurement and labor for installing new equipment, cabling, and testing/certifying. The Horizontal (workstation) Cabling System shall consist of 4-pair Unshielded Twisted Pair (UTP) Copper Cables to each work area outlet unless otherwise noted for specific locations.  The cables shall be installed from the Work Area Outlet to the respective IT Closet (noted on drawing), and routed to the appropriate rack and terminated. There will be OM3 6 strand cable with innerduct pulled and terminated from demarc room to the IT Closet (approx. distance 100’). The contractor awarded the bid will be Panduit certified and supplied our labeling scheme for cable, rack, and patch panels.

Qualified Bidder must include:

- Panduit Certification

- Breakout cost of Contractor Provided material

- Cost of Material and Labor are to be listed separate according to the drawing.

- Cost of Material and Labor for additional drop if needed.

Components:

- Contractor Provided

| Part | Part# | Amount | Description |
| --- | --- | --- | --- |
| Panduit Cat 6 | PUP6004BL-UY | Per Drawing | Cat 6 Cable Black |
| Panduit RJ45 8 Position | CJ688TGBU | Per Drawing | Data Jacks |
| Panduit RJ45 8 Positon | CJ688TGOR | Per Drawing | AP Jacks |
| Panduit Wall Plate or Surface Box | If needed | NA | Match wall color |
| Panduit Rack Enclosure | FRME1U | 1 | Fiber Rack Enclosure |
| Panduit Wall Enclosure | FWME2 | 1 | Fiber Wall Enclosure |
| Ladder Rack | Vendor Preference |  | Enough for wall and one rack |
| Panduit OM3 Fiber | FOCPX06Y |  | 6 strand OM3 In/Outdoor fiber cable |
| Innerduct | Vendor Preference |  | Innerduct for 6 strand fiber |
| Panduit Coupler Panel | FAP6WAQDLC | 1 | Fiber coupler panel |
| Panduit Vertical wire management | WMPHVHC45E | 1 | 6" wide vertical cable management |
| Panduit rack | R2P | 1 | 2 post rack |
| Panduit horizontal wire management | WMPFSE | 3 | 1u cable management |
| Panduit empty angled 48port pa | CPPLA48WBLY | 1 | Patch Panel |
| APC ATS | AP4450 | 1 | Automatic Transfer Switch |
| APC UPS 1500 | SMX1500RM2UNC | 1 | Uninterruptible Power Supply |

- Miscellaneous – Contractor will provide all miscellaneous components as mentioned above as “Contractor Provided” to complete the install. This includes, but not limited to, cables, connectors, j-hooks, brackets, custom panels, racks, labels, hardware, tie wraps, etc. This is a TURN KEY install.

Tasks:

  - Data Cable Pulls - Contractor will install, terminate, test, and certify all cabling needed to complete the project.  Data drops (blue triangle on drawing) will have Panduit Blue Jacks and AP drops (orange triangle on drawing) will have Panduit Orange Jacks. Provide a PDF file showing certification of all data cables.

  - Fiber Cable w/innerduct Pull – Contractor will install fiber enclosures in IT closet and also at the demarc.  Contractor will install, terminate Panduit OM3 6 strand cable with Panduit LC connectors, test, and certify. The approximate distance from demarc to IT Closet is 100’. Provide a PDF file showing certification of all fiber cables.

  - IT Closet – Contractor will provide and install all material required to complete the infrastructure system as stated in Component section.

  - Demarc – Contractor will install all material required to complete the infrastructure system as stated in Component section.

Deliverables:

- Contractor shall warrant for 1(one) year all materials, equipment and/or services delivered to be free from defect of material or workmanship.

- Furnish on a PDF file showing certification on all cables to owner.

- Provide pictures of Demarc and IT closet install.

Key Assumptions

- Contractor/Installer will be Panduit certified to install and terminate cable.

- Contractor has all necessary tools to accomplish service request.

- Contractor understands and agrees to late night and/or overnight working hours if needed.