Scope of Work.

Cherokee Nation Entertainment is seeking qualified Fencing Contractors to provide labor and materials to construct a chain link fence along the perimeter of the 5th floor of the parking garage at the Hard Rock Hotel and Casino in Catoosa, Oklahoma.

The work will consist of:

Purchasing and installing post and fence netting on the top level of the parking garage

- Contractor is to provide all necessary wire, post, panels, and structural support to complete a 9.5 foot tall fence.

- Estimated length is 1,120LF.  Contractor is to verify.

- Posts can be mounted to the interior face of the parapet wall or the top through the use of an approved anchoring system.

- A top and bottom rail to be used for support.

- Top is to tilt inward.

- Material options are: Galvanized, Galvanized with vinyl fabric, Black powder coated post and vinyl fabric.

Selected firm will work with Cherokee Nation Businesses Corporate Construction, Cherokee Nation Entertainment Operations and Security on issues or concerns as necessary.

Fees

The fee is to be a lump sum cost. The cost is to be all inclusive and is to broken down into Labor and Materials.