Cherokee Nation Entertainment

Statement of Work

6/19/2020

Presented by:

Stephen Goodell

Time and materials

| Owner Name | Cherokee Nation Entertainment |
| --- | --- |
| Owner Address | 20900 S 4200 Rd |
| Project name | Sewer Line Installation |
| Engagement duration | Turn Key |
| Begin date | 7-1-2020 |
| End date | 7-10-2020 |

| Item description | Unit Information |  |
| --- | --- | --- |
| Sewer Line Installation | See image |  |

Description:

CNE requires the existing aerobic system located at the Test Barn be removed (Item D) and be backfilled to 85% compaction. Test Barn sink, restroom, and lavatory will connect to the new sewer service. Contractor to provide waste piping to all noted fixtures.

Contractor shall provide all trenching from Point A to Point B to Point C and provide connection to existing manhole at Point C. When crossing road, Point E, follow detail below.  The new sewer main shall be 6” schedule 40 PVC pipe installed with a 1/8” per foot slope to drain. Sewer line shall be bedded with 4” of sand above the pipe and 4” of sand below the invert elevation. Contractor is responsible for grouting and making leak tight any connection to the existing manhole. The line shall have 2-way clean out tees every 100’.  Contractor installation shall be in compliance with the 2015 International Plumbing Code, or as adopted by the local jurisdiction.   Contractor will include excavating along with trench boxes as required.  All parts supplied by contractor. Pipe distance is estimated to be 561’. Contractor is encouraged to conduct a site visit to determine actual quantities.

Contractor will be required to have a current Oklahoma Horse Racing Commission (OHRC) license. If Contractor does not currently possess an OHRC license, Owner will reimburse the Contractor for the direct fee of the license. Any and all permits will be the responsibility of the Contractor.

Item E Detail

Project Contact:  Stephen Goodell

Once bid is awarded schedule will be coordinated with Stephen Goodell.

All questions are to be submitted via email to Tina Jones at tina.jones@cnent.com.

Statement of work

Assumptions

All materials, tools, and labor will be provide by vendor.  Any material cost that are extra with job should be listed as side note expense.

Change management process

Any changes in the job will be addressed with Stephen Goodell and any added expenses will need to have a change order put in for unseen cost.  All cost must provide a statement of need and list in detail what expenses cover.

Engagement related expenses

TERO Fees of ½ of 1% of total bid amount and $25 per day for each Non-Native (must have a valid CDIB card) is to be included in bid. Awarded company, and workers, will also be required to have an Oklahoma Horse Racing Commission license before any work on property can be done.